## Slide 1: AT-1724 Allison Transmission, Inc. Global Transport Label Standard
AT 1724A – Individual Container
AT 1724B – MASTER Container
AT 1724C – MIXED LOAD Container

## Slide 2
SPECIFIC CRITERIA FOR THE ALLISON TRANSMISSION (ATI) GLOBAL TRADING PARTNER LABEL TEMPLATE:
THE TEMPLATES IDENTIFIES HOW AND WHERE DATA IS TO BE PLACED ON THE LABEL WHEN IT IS REQUIRED AS PART OF A ATI BUSINESS REQUIREMENT:
        1724A IS FOR INDIVIDUAL CONTAINERS OF LIKE PARTS
        1724B IS FOR MASTER LABEL – CONTAINER OF INDIVIDUAL CONTAINERS OF LIKE PARTS
        1724C IS FOR MIXED LOAD LABEL – CONTAINER OF INDIVDUAL CONTAINERS OF UNLIKE PARTS
FONT SIZES ARE SPECIFIED FOR READABILITY - DATA THAT WILL NOT FIT AT THE SPECIFIED FONT SIZE IS TO BE TRUNCATED OR ABREVIATED.
WHEN A MATERIAL HANDLING CODE (ALSO KNOWN AS “DLOC” / Allison Plant Delivery Location) IS REQUIRED, RECEIVING LOCATIONS ARE RESPONSIBLE FOR PROVIDING THE CORRECT INFORMATION TO THE SUPPLIER (VIA EDI)
LABEL DIMENSIONS ARE NOMINAL -
        A6/AIAG IS APPROXIMATELY 102 MM (4”) HIGH BY” 152 (6 MM) WIDE
        A5 IS APPROXIMATELY 148 MM (5.80”) HIGH BY 210 MM (8.25”) WIDE
        REDUCED HEIGHT LABEL IS APPROXIMATELY 74 MM (2.9”) HIGH X 210 MM (8.25”)
LABELS SHALL BE PRINTED WITH BLACK CHARACTERS ON WHITE BACKGROUND (NEITHER COLORED STOCK NOR COLORED INK IS ALLOWED)
FONTS SHALL BE UPPERCASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
BAR CODE SYMBOLOGIES ON THE LABEL SHALL BE: CODE 128 LINEAR BAR CODE, AND, PDF417 2-D BAR CODE
DATES SHALL BE IN THE INTERNATIONAL FORMAT OF “DDMMMYYYY” (Ex: 25SEP2001)
GROSS WEIGHT SHALL BE EXPRESSED IN LBS (ROUNDED, NO DECIMAL)
LABELS SHALL BE VERIFIED AS LEGIBLE BY THE SUPPLIER PER AIAG (B10, B14, B8, B16), ODETTE, QS9000 AND ISO STANDARDS
(NOTE: BAR CODES MUST BE EASILY SCANNABLE AND MEET OR EXCEED ISO PRINT QUALITY “C” AT POINT OF RECEIPT)
LABELS SHALL BE AFFIXED IN ACCORDANCE WITH AT1700 GUIDELINES (USUALLY OPPOSITE ENDS OF EACH CONTAINER)
THIS DOCUMENT IS AVAILABLE AT ALLISONTRANSMISSION.COM
FOR ADDITIONAL INFORMATION PLEASE CONTACT ATI BUYER OR CONTAINER PACKAGING ENGINEER
NOTE: SEE ALSO MASTER LABEL (AT1724-B) AND
MIXED LABEL (AT1724-C) STANDARDS
AND PACKAGING GUIDELINES AT1700
PAGE 2
AT 1724: LABEL TEMPLATE
FOR CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A CONTAINER HOLDING
ONE OR MORE PARTS WITH A SINGLE OR MULTIPLE PART NUMBERS.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
15AUG2015
2015-08
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
Notes: 1

## Slide 3
PDF 417 2D BAR CODE
DATA SYNTAX STRUCTURE
[)>RS06GSP12345678GSQ160GS1JUN123456789A2B4C6D8EGS20LA6-987GS21LLC 15CGS15KG1155GSBKLT3214GS7Q10GTRSEOT
MESSAGE
HEADER
FORMAT
HEADER
GROUP
SEPARATOR
GS
DATA
FORMAT
06 = DIs
RECORD
SEPARATOR
RS
COMPLIANCE
INDICATOR
[)>
RECORD
SEPARATOR
RS
MESSAGE
TRAILER
EoT
FOR MORE DETAILS REFER TO AIAG B14
PAGE 3
AT 1724 LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724
15AUG2015
2015-08
Notes: 9

## Slide 4
DATA IDENTIFIERS
DATA IDENTIFIERS (DIs) DEFINE THE NATURE OF THE DATA CONTAINED WITHIN THE LINEAR BAR CODE.
DIs ARE USED WITHIN THE 2D BAR CODE TO DEFINE THE NATURE OF THE DATA IN EACH FIELD.
THE TABLE BELOW REPRESENT TYPICAL DIs USED WITH ATI COMMON GLOBAL SHIPPING LABEL TEMPLATES.
ADDITIONAL DIs MAY BE USED AS BUSINESS PROCESSES REQUIRE AND SHALL CONFORM TO AIAG B10, B14, ANSI, AND ISO STANDARDS
PAGE 4
AT 1724 LABEL
TEMPLATE FOR MASTER CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET HOLDING ONE OR MORE CONTAINERS OF A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724
15AUG2015
2015-08
DATA IDENTIFIER (DI) | QUALIFIER | DEFINITION | COMMENT | EXAMPLE | MAX LENGTH | WITHIN 2D BAR CODE
P | na | AT PART NUMBER | ALPHA NUMERIC | 123456789 | 18 | REQUIRED
Q | na | QUANTITY | QUANTITY PER PACK | Q1000 |  | REQUIRED
7Q | PL | TOTAL QUANITY | TOTAL QUANTITY IN MASTER PACK | 7Q10000PL |  | REQUIRED
7Q | PK | NUMBER OF PACKS | NUMBER OF INDIVIDUAL PCKS IN MASTER PACK | 7Q10PK |  | REQUIRED
7Q | GT | GROSS WEIGHT | GROSS WEIGHT ROUNDED (NO DECIMALS) | 7Q999GT |  | REQUIRED
1J or 6J or 5J | na | MASTER LICENSE PLATE | HAS STRUCTURE SEE CODE 128 BAR CODE STRUCTURE FOR LICENSE PLATE | 6JUN12345678A2B4C6D8E |  | REQUIRED
20L | na | MATERIAL HANDLING CODE | DELIVERY LOCATION WITHING PLANT | 20LA6-987 | 18 | REQUIRED IF PROVIDED
21L | na | DOCK CODE | IDENTIFIES RECEIVING DOCK | 21LLC 15C | 8 | REQUIRED IF PROVIDED
K | na | PO NUMBER & PO LINE NUMBER | IF REQUIRED AS PART OF AT BUSINESS PROCESS | KG1234-00120 | 16 | REQUIRED IF PROVIDED
15K | na | KANBAN NUMBER | IF REQUIRED AS PART OF AT BUSINESS PROCESS | 15Kg1155 |  | REQUIRED IF PROVIDED
B | na | CONTAINER TYPE | ATI SPECIFIED CONTAINER NUMBER OR IF NOT SPECIFIED, USE SUPPLIER REFERENCE SUCH AS A CARTON | BKLT314 |  | REQUIRED FOR 1724 A
2S | na | SHIPMENT ID (SID)/PICK-UP SHEET NUMBER | CREATED BY SUPPLIER AND TRANSMITTED IN THE ASN | B03456789 |  | OPTIONAL
Notes: 8

## Slide 5
1JUN123456789A2B4C6D8E
Scanned Data Stream
Serial number
1J: Data Identifier
UN: Assigning Authority D-U-N-S
D-U-N-S number
CODE 128 BAR CODE STRUCTURE
FOR LICENSE PLATE
CODE 128 SPECIFICATION:
‘X’ DIMENSION SHALL BE IN THE RANGE OF 0.33 MM (0.013 INCH) TO 0.43 MM (0.017 INCH)
BAR CODE HEIGHT SHALL BE A MINIMUM OF 13 MM (0.5 INCH)
QUIET ZONE (AREA AT EACH END OF BAR CODE) SHALL BE A MINIMUM OF 6.3 MM (0.25 INCH)
BAR CODE SHALL MEET A MINIMUM ANSI PRINT QUALITY GRADE OF ‘C’
LICENSE PLATE (1J)
UN 123456789 A2B4C6D8E
9-character maximum
Unique container serial number
- generated by supplier
leading zeros not recommended
- not to be repeated for period of
1 year
ISO Assigning authority
UN = D-U-N-S:
- assigned by Dun & Bradstreet.
9-character D-U-N-S number
- manufacturing site specific
- fixed; should never have to be changed
Data Identifier:
1J: Individual container of like parts
6J: MASTER - Container of individual containers of like parts
5J: MIXED LOAD – Container of individual containers of unlike parts
1J
PAGE 5
AT 1724: LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724
15AUG2015
2015-08
Notes: 7

## Slide 6
PDF 417 2D BAR CODE
TECHNICAL SPECIFICATIONS
1X
Y=3X
SPECIFICATION:
‘X’ DIMENSION = MIN 0.010 INCH (10 MILS) (0.254 MM)
4 12
NOMINAL 7 COLUMNS
HEIGHT: 1.0 IN ± 0.2 IN (25.40 MM ± 5.08 MM) INCLUDING ALL-AROUND QUIET ZONE OF 0.04 IN (1MM) MUST FIT WITHIN SINGLE SUB-BLOCK
ERROR CORRECTION (SECURITY) LEVEL SHALL BE 5, 4, 0R 3
USE THE MAX ECC THAT WILLPRINT AND SCAN IN 2D LOCATION
Note: Bar code enlarged for
illustration purposes only
IT’S YOUR IMAGE
Your label is the first impression of your company and its products.
Poorly printed labels, sloppy placement, and un-scanable
bar codes reflect on the perception of your company.
The shipping label and associated process should
receive the same quality efforts as your product - it’s your image.
PAGE 6
AT 1724: LABEL
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724
15AUG2015
2015-08
Notes: 10

## Slide 7: AT 1724 – A Individual Container

## Slide 8
LABEL DIMENSIONS ARE NOMINAL - APPROXIMATELY 4” (102 MM) HIGH BY 6” (152 MM) WIDE
DATA LAYOUT
A1
SHIP FROM
A2
SHIP TO
A3
2D SYMBOL
REFERENCE #1
B2
ROUTING
INFORMATION
B3
LOGISTICS REFERENCE
C
ATI PART NUMBER
D1
LICENSE PLATE
D2
REFERENCE #2
E1
SUPPLIER AREA
It is recommended that this vertical
separator line should not be printed.
(See Quiet Zone)
PAGE 8
AT 1724-A: LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-A
15AUG2015
2015-08
Notes: 2

## Slide 9
0
0
38 mm
(1.5 in)
96.5 mm
(3.8 in)
48 mm
1.89 in
102 mm
(4.02 in)
106 mm
(4.17 in)
25.4 mm
(1.0 in)
38.1 mm
(1.5 in)
50.8 mm
(2.0 in)
76.2 mm
(3.0 in)
*
*This dimension based on nominal 0.38 mm (0.015 in) Code 128 bar code license plate. The label provider must ensure quiet zone requirement of 6.4 mm (0.25 in ) is maintained.
A1
A2
A3
B1
B2
B3
C
D1
D2
E1
LABEL DIMENSIONS ARE NOMINAL - APPROXIMATELY 4” (102 MM) HIGH BY 6” (152 MM) WIDE
PAGE 9
AT 1724-A: LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-A
15AUG2015
2015-08

## Slide 10
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
EMAIL PHONE CONTACT
ASSEMBLED/MADE IN XX
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
DOCK 33
160
QUANTITY:
MATERIAL HANDLING CODE:
REFERENCE:
PART
NUMBER
12345678
LICENSE PLATE (1J)
UN 123456789 A2B4C6D8E
DATE PACKAGED:
24SEP2001
CONTAINER TYPE:
SC151208
GROSS WEIGHT:
10 KG
FONTS SHALL BE UPPER CASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
DATA SOURCES FOR EDI SUPPLIERS
ADDRESS INFORMATION
SUPPLIER GENERATED BASED ON CUSTOMER ORDER
DOCK CODE FROM
EDIFACT DELFOR LOC SEGMENT
DATA FROM SUPPLIER FILES
CUSTOMER PART NUMBER MUST MATCH CUSTOMER ORDER
DATA FROM SUPPLIER FILES
(QUANTITY SHOULD MATCH
CUSTOMER ORDER)
SUPPLIER DUNS ID COMBINED WITH SUPPLIER GENERATED SHIP PACK SERIAL NUMBER
UNRESTRICTED AREA OF LABEL FOR SUPPLIER’S USE
NOTE - USE APPROPRATE DIs AND DATA SYNTAX FOR ALL BAR CODES
DATA FROM SUPPLIER NOTE: SUPPLIER CONTACT (PHONE OR E-MAIL) IS OPTIONAL
NOTE: PCI INFORMATION QUALIFIED IN COMPOSITE DATA ELEMENT C827/7511; DATA PROVIDED IN COMPOSITE DATA ELEMENT C210/7102
REFERENCE SUB-BLOCK #2
DATE: SPECIFY TYPE, E.G. SHIP, PACK, MANUFACTURING
SUPPLIER GENERATED
CONTAINER TYPE:
SUPPLIER GENERATED
BASED ON CUSTOMER
REQUIREMENTS
GROSS WEIGHT:
SUPPLIER GENERATED ROUND – NO DECIMAL
MATERIAL HANDLING CODE FROM
EDIFACT DELFOR PCI SEGMENT
REFERENCE SUB-BLOCK #1
CUSTOMER REQUESTED PO NUMBER AND PO LINE NUMBER FROM DELFOR RFF SEGMENTS
OPTIONAL SPECIAL SYMBOL (EG: CRITICAL PART, SAFETY, ETC.)
ENCODED 2D BAR CODE DATA SHALL INCLUDE PART NUMBER, PART QUANTITY, LICENSE PLATE,
DOCK, MATERIAL HANDLING CODE,
REFERENCE#1 (DEPENDS ON BUSINESS REQUIREMENT).
ADDITIONAL RECOMMENDED DATA:, CONTAINER TYPE, WEIGHT
PAGE 10
AT 1724-A: LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-A
15AUG2015
2015-08
06A81 RACK 01
504123-00120
Notes: 3

## Slide 11
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
EMAIL PHONE CONTACT
ASSEMBLED/MADE IN XX
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
DOCK 33
160
QUANTITY:
MATERIAL HANDLING CODE:
REFERENCE:
PART
NUMBER
12345678
LICENSE PLATE (1J)
UN 123456789 A2B4C6D8E
DATE PACKAGED:
24SEP2001
CONTAINER TYPE:
SC151208
GROSS WEIGHT:
10 KG
FONTS SHALL BE UPPER CASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
DATA SOURCES FOR NON EDI SUPPLIERS
ADDRESS INFORMATION
SUPPLIER GENERATED BASED
ATI PO LINE SHIPPING ADDRESS
DATA FROM SUPPLIER FILES
CUSTOMER PART NUMBER MUST MATCH CUSTOMER ORDER
DATA FROM SUPPLIER FILES
(QUANTITY SHOULD MATCH
CUSTOMER ORDER)
SUPPLIER DUNS ID COMBINED WITH SUPPLIER GENERATED SHIP PACK SERIAL NUMBER
UNRESTRICTED AREA OF LABEL FOR SUPPLIER’S USE
NOTE - USE APPROPRATE DIs AND DATA SYNTAX FOR ALL BAR CODES
DATA FROM SUPPLIER
NOTE: SUPPLIER CONTACT (PHONE OR E-MAIL) IS OPTIONAL
REFERENCE SUB-BLOCK #2
DATE: SPECIFY TYPE, E.G. SHIP, PACK, MANUFACTURING
SUPPLIER GENERATED
CONTAINER TYPE:
SUPPLIER GENERATED
BASED ON CUSTOMER
REQUIREMENTS
GROSS WEIGHT:IN KG
SUPPLIER GENERATED ROUND – NO DECIMAL
MATERIAL HANDLING CODE
REFERENCE SUB-BLOCK #1
CUSTOMER REQUESTED PO NUMBER AND PO LINE NUMBER
OPTIONAL SPECIAL SYMBOL (EG: CRITICAL PART, SAFETY, ETC.)
ENCODED 2D BAR CODE DATA SHALL INCLUDE PART NUMBER, PART QUANTITY, LICENSE PLATE,
DOCK, MATERIAL HANDLING CODE,
REFERENCE#1 (DEPENDS ON BUSINESS REQUIREMENT).
ADDITIONAL RECOMMENDED DATA:, CONTAINER TYPE, WEIGHT
PAGE 11
AT 1724-A: LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-A
15AUG2015
2015-08
06A81 RACK 01
504123-00120
Notes: 3

## Slide 12
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
EMAIL PHONE CONTACT
ASSEMBLED/MADE IN XX
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
/DOCK:
DOCK 33
160
QUANTITY:
06A81 RACK 01
MATERIAL HANDLING CODE:
504123-00120
PURCHASE ORDER:
PART
NUMBER
12345678
LICENSE PLATE (1J)
UN 123456789 A2B4C6D8E
DATE: PACKAGED
24SEP2001
CONTAINER TYPE:
SC151208
GROSS WEIGHT:
10 KG
FONTS SHALL BE UPPER CASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
Title: FROM:
6 Point, 1.5 mm, 0.06"
Address 4 lines max
10 point, 2.5 mm, 0.1"
Phone Number (Optional)
10 Point, 2.5 mm, 0.1"
MADE IN XXX or ASY IN XXX
10 Point, 2.5 mm, 0.1"
Title: QUANTITY
6 Point
Text
36 Point
Title: None
PDF 417 2D Bar Code per AIAG B-16
Title: LICENSE PLATE (1J)
6 Point
Bar Code
Code 128
0.381 mm (15 mil) nominal
Height 13 mm (0.5 inch) min
Data Identifier: 1J
Assigning Authority: UN = D-U-N-S
9 digits D-U-N-S Number
9 characters container serial
number max
Human Readable Text
24 Point
Note-Spaces are optional in human readable text only. SPACES SHALL NOT BE INCLUDED IN BAR CODE DATA
Reference Sub-Block #2
Title: DATE PACKAGED
6 Point.
Date Text (9 Characters)
26 Point
Title: CONTAINER TYPE
6 Point
Container Type
14 Point,
Title: GROSS WEIGHT
6 Point,
Gross Weight Text
14 Point
Unit of Weight Text KG
14 Point
Mat Handling Reference Sub-Block
Title: MATERIAL HANDLING CODE
6 Point
MATERIAL HANDLING CODE Text
18 Character max
16 Point
Title: TO:
6 Point
Address 4 lines max
12 Point
Title ; DOCK
6 Point
Dock Text
8 Character max
28 Point
1724-A FORMAT & FONT SPECS
Title: PART
NUMBER
6 Point
Part Number Text
44 Point
Graphic Optional
Safety/Security
Right Justified
Max Number of Characters:18
PAGE 12
AT 1724-A: LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
Reference Sub-Block #1
Title: REFERENCE
6 Point
REFERENCE Text
10 Character max
24 Point
15AUG2015
2015-08
Notes: 4

## Slide 13
A1
A2
A3
B1
B2
B3
C
D1
D2
E1
E2
0
0
25.4 mm
(1.0 in)
38.1 mm
(1.5 in)
76.2 mm
(3.0 in)
43 mm
(1.65 in)
101.5 mm
(4.0 in)
153 mm
(6.0 in)
107 mm
(14.3 in)CV
111 mm
(4.4 in)
Shaded area 5 mm (0.2 in) wide
clearance for label holder
53 mm
(2.1 in)
DATA LAYOUT
for SMALL CONTAINERS (example KLT)
(Alternate format to be used at supplier’s option when shipping parts in small containers)
74mm (3”) x 210mm (8”) label or equivalent
PAGE 13
AT 1724-A: LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-A
15AUG2015
2015-08
Notes: 5

## Slide 14
FORMAT SPECIFICATIONS
for SMALL CONTAINERS (example KLT)
(Alternate format to be used at supplier’s option when shipping parts in small containers)
74mm (3”) x 210mm (8”) label or equivalent
(Data Sources & Fonts Are The Same As On Pages 3 & 4)
E1
SUPPLIER
Shaded area 5 mm (0.2 in) wide is clearance for label holder
It is recommended that these vertical
separator lines should not be printed.
(See Quiet Zone)
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
EMAIL PHONE CONTACT
ASSEMBLED/MADE IN XX
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
DOCK 33
160
QUANTITY:
MATERIAL HANDLING CODE:
REFERENCE:
LICENSE PLATE (1J)
UN 123456789 A2B4C6D8E
DATE PACKAGED:
24SEP2001
CONTAINER TYPE:
SC151208
GROSS WEIGHT:
10 KG
PART
NUMBER
12345678
PAGE 14
AT 1724-A: LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-A
15AUG2015
2015-08
06A81 RACK 01
504123-00120
Notes: 6

## Slide 15
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
EMAIL PHONE CONTACT
ASSEMBLED/MADE IN XX
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
DOCK 33
160
QUANTITY:
MATERIAL HANDLING CODE:
REFERENCE:
PART
NUMBER
12345678
LICENSE PLATE (1J)
UN 123456789 A2B4C6D8E
DATE PACKAGED:
24SEP2001
CONTAINER TYPE:
SC151208
GROSS WEIGHT:
10 KG
41L65
GREEN WIDGET
STOCKMAN 21
EDI PCI SEGMENT
11Z
LOC
PAGE 15
AT 1724-A: LABEL
TEMPLATE FOR INDIVIDUAL CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A SINGLE CONTAINER
HOLDING ONE OR MORE PARTS WITH A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-A
15AUG2015
2015-08
06A81 RACK 01
504123-00120
UNB+UNOA:1+XXXXXXXXX:01+XXXXXXXXX:01+150501:0152+2966++++1
UNG+DELFOR+XXXXXXXXX+XXXXXXXXX+150501:0152+1+UN+D97:7A
UNH+1+DELFOR:D:97A:UN
BGM+241:::SH+20150501+5
DTM+158:20010101:102
DTM+159:20151231:102
DTM+137:20150501:102
NAD+MI+XXXXXXXXX::16
NAD+SU+XXXXX::92
NAD+ST+XXXXXXXX::86
GIS+37
LIN+++12345678:IN
LOC+11+12
RFF+ON:0000504123
RFF+RE:1003
RFF+LI:00020
PAC++++A:EXP 16X12X04:RC
PCI++06A81 RACK 01++11Z::167
NAD+MI+ALLISON TRANSMISSION DIVISION::92
CTA+IC+:John Doe FAX 317-242-0000
COM+317-555-1234:TE
QTY+48:576:EA
DTM+50:20150309:102
QTY+70:72255:EA
DTM+51:20010101:102
DTM+52:20151231:102
QTY+61:240:EA
DTM+51:20010101:102
DTM+52:20151231:102
SCC+2
QTY+1:0:EA
DTM+52:20150522:102
SCC+3
QTY+1:0:EA
DTM+52:20150730:102
SCC+1++D
QTY+1:288:EA
DTM+10:20150521:102
SCC+4++W
QTY+1:0:EA
DTM+10:20150608:102
< segments removed for this example >
UNT+70+1
UNE+1+1
UNZ+1+2966
LOC
11Z
Notes: 11

## Slide 16: AT 1724 – B MASTER Container

## Slide 17
LABEL DIMENSIONS ARE NOMINAL - APPROXIMATELY 4” (102 MM) HIGH BY 6” (152 MM) WIDE
DATA LAYOUT
MASTER
LABEL
FROM
TO
2D
BAR CODE
MATERIAL
HANDLING CODE
PART NUMBER
6J LICENSE PLATE
LOGISTICS
DATA
PAGE 17
AT 1724-B: LABEL
TEMPLATE FOR MASTER CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET HOLDING ONE OR MORE CONTAINERS OF A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-B
15AUG2015
2015-08
Notes: 2

## Slide 18
*This dimension based on nominal 0.38 mm (0.015 in) Code 128 bar code license plate. The label provider must ensure quiet zone requirement of 6.4 mm (0.25 in ) is maintained.
LABEL DIMENSIONS ARE NOMINAL - APPROXIMATELY 4” (102 MM) HIGH BY 6” (152 MM) WIDE
0
0
38 mm
(1.5 in)
48 mm
1.89 in
102 mm
(4.02 in)
106 mm
(4.17 in)
25.4 mm
(1.0 in)
38.1 mm
(1.5 in)
50.8 mm
(2.0 in)
76.2 mm
(3.0 in)
*
A1
FROM
A2
TO
2D
BAR CODE
MATERIAL
HANDLING CODE
C
PART NUMBER
D1
6J LICENSE PLATE
1D BAR CODE
D2
LOGISTICS
DATA
MASTER
LABEL
PAGE 18
AT 1724-B: LABEL
TEMPLATE FOR MASTER CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET HOLDING ONE OR MORE CONTAINERS OF A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-B
15AUG2015
2015-08

## Slide 19
LICENSE PLATE (6J):
UN 123456789 A2B4C6D8E
PART #:
12345678
MATERIAL HANDLING CODE:
MASTER
LABEL
GROSS WEIGHT KG :
# PACKS :
QTY/PACK :
TOTAL QTY :
999
10000
10
1000
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
EMAIL PHONE CONTACT
ASSEMBLED/MADE IN XX
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
DOCK 33
FONTS SHALL BE UPPER CASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
NON-EDI DATA SOURCES
ADDRESS INFORMATION
SUPPLIER GENERATED BASED ON CUSTOMER ORDER
DATA FROM SUPPLIER FILES
CUSTOMER PART NUMBER MUST MATCH CUSTOMER ORDER
SUPPLIER DUNS ID COMBINED WITH SUPPLIER GENERATED SHIP PACK SERIAL NUMBER
DATA FROM SUPPLIER FILES
NOTE: SUPPLIER CONTACT (PHONE OR E-MAIL) IS AT THE SUPPLIER’S OPTION
LOGISTICS DATA
GROSS WEIGHT:
SUPPLIER GENERATED ROUND – NO DECIMAL
TOTAL QUANTITY:
SUPPLIER GENERATED
NUMBER OF PACKS:
SUPPLIER GENERATED
QUANTITY PER PACK:
SUPPLIER GENERATED
MATERIAL HANDLING CODE
PAGE 19
AT 1724-B: LABEL
TEMPLATE FOR MASTER CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET HOLDING ONE OR MORE CONTAINERS OF A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-B
15AUG2015
2015-08
06A81 RACK 01
Notes: 3

## Slide 20
LICENSE PLATE (6J):
UN 123456789 A2B4C6D8E
PART #:
12345678
MATERIAL HANDLING CODE:
MASTER
LABEL
GROSS WEIGHT KG :
# PACKS :
QTY/PACK :
TOTAL QTY :
999
10000
10
1000
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
EMAIL PHONE CONTACT
ASSEMBLED/MADE IN XX
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
DOCK 33
FONTS SHALL BE UPPER CASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
EDI DATA SOURCES
ADDRESS INFORMATION
SUPPLIER GENERATED BASED ON CUSTOMER ORDER
DOCK CODE FROM
EDIFACT DELFOR LOC SEGMENT
DATA FROM SUPPLIER FILES
CUSTOMER PART NUMBER MUST MATCH CUSTOMER ORDER
SUPPLIER DUNS ID COMBINED WITH SUPPLIER GENERATED SHIP PACK SERIAL NUMBER
DATA FROM SUPPLIER NOTE: SUPPLIER CONTACT (PHONE OR E-MAIL)
NOTE: PCI INFORMATION QUALIFIED IN COMPOSITE DATA ELEMENT C827/7511; DATA PROVIDED IN COMPOSITE DATA ELEMENT C210/7102
LOGISTICS DATA
GROSS WEIGHT:
SUPPLIER GENERATED ROUND – NO DECIMAL
TOTAL QUANTITY:
SUPPLIER GENERATED
NUMBER OF PACKS:
SUPPLIER GENERATED
QUANTITY PER PACK:
SUPPLIER GENERATED
MATERIAL HANDLING CODE FROM
EDIFACT DELFOR PCI SEGMENT
PAGE 20
AT 1724-B: LABEL
TEMPLATE FOR MASTER CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET HOLDING ONE OR MORE CONTAINERS OF A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-B
15AUG2015
2015-08
06A81 RACK 01
Notes: 3

## Slide 21
LICENSE PLATE (6J):
UN 123456789 A2B4C6D8E
PART #:
12345678
MATERIAL HANDLING CODE:
MASTER
LABEL
GROSS WEIGHT KG :
# PACKS :
QTY/PACK :
TOTAL QTY :
999
10000
10
1000
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
EMAIL PHONE CONTACT
ASSEMBLED/MADE IN XX
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
DOCK 33
FONTS SHALL BE UPPER CASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
Title: FROM:
6 Point, 1.5 mm, 0.06"
Address 4 lines max
10 point, 2.5 mm, 0.1"
Phone Number (Optional)
10 Point, 2.5 mm, 0.1"
MADE IN XXX or ASY IN XXX
10 Point, 2.5 mm, 0.1"
Title: QUANTITY
6 Point, 1.5 mm, 0.1”
Text
36 Point, 9.17mm, 0.36”
2D Bar Code per AIAG B-16
Title: LICENSE PLATE (1J)
6 Point, 1.5 mm, 0.06"
Bar Code
Code 128
0.381 mm (15 mil) nominal
Height 13 mm (0.5 inch) min
Data Identifier: 6J
Assigning Authority: UN = D-U-N-S
9 digits D-U-N-S Number
9 characters container serial
number max
Human Readable Text
24 Point , 6.1 mm, 0.24”
Note-Spaces are optional in human readable text only. SPACES SHALL NOT BE INCLUDED IN BAR CODE DATA
Reference Sub-Block #2
Title: DATE PACKAGED
6 Point, 1.5 mm, 0.06"
Date Text (9 Characters)
18 Point, 6.4 mm, 0..25”
Title: CONTAINER TYPE
6 Point, 1.5 mm, 0.06”
Container Type
18 Point, 6.4 mm, 0..25”
Title: GROSS WEIGHT
6 Point, 1.5 mm, 0.06”
Gross Weight Text
18 Point, 6.4 mm, 0..25”
Unit of Weight Text KG
18 Point, 6.4 mm, 0..25”
Mat Handling Reference Sub-Block
Title: MATERIAL HANDLING CODE
6 Point, 1.5 mm, 0.06"
MATERIAL HANDLING CODE Text
18 Character max
36 Point, 9.17mm, 0.36”
Reference Sub-Block #1
Title: REFERENCE
6 Point, 1.5 mm, 0.06"
REFERENCE Text
10 Character max
36 Point, 9.1 mm, 0.36”
Title: TO:
6 Point, 1.5 mm, 0.06"
Address 4 lines max
12 Point, 4.3 mm, 0..17”
Title ; DOCK
12 Point, 1.5 mm, 0.06"
Dock Text
8 Character max
28 Point, 6.4 mm, 0..25"
1724-B FORMAT & FONT SPECS
Title: PART
NUMBER
6 Point, 1.5 mm, 0.06"
Part Number Text
44 Point, 11.2 mm, 0.44”
Graphic Optional
Safety/Security
Right Justified
PAGE 21
AT 1724-B: LABEL
TEMPLATE FOR MASTER CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET HOLDING ONE OR MORE CONTAINERS OF A SINGLE PART NUMBER.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
15AUG2015
2015-08
06A81 RACK 01
Notes: 4

## Slide 22: AT 1724 – C MIXED LOAD Container

## Slide 23
LABEL DIMENSIONS ARE NOMINAL - APPROXIMATELY 4” (102 MM) HIGH BY 6” (152 MM) WIDE
DATA LAYOUT
MIXED
LABEL
PAGE 23
AT 1724-C: LABEL
TEMPLATE FOR MIXED LOAD CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET WHEN MORE THAN ONE PART NUMBER IS CONTAINED BY THE MASTER CONTAINER OR PALLET.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
FROM
TO
2D
BAR CODE
5J LICENSE PLATE
1D BAR CODE
LOGISTICS
DATA
PART A
PART B
PART C
PART D
PART E
PART F
PART G
PART H
1724-C
15AUG2015
2015-08
Notes: 2

## Slide 24
*This dimension based on nominal 0.38 mm (0.015 in) Code 128 bar code license plate. The label provider must ensure quiet zone requirement of 6.4 mm (0.25 in ) is maintained.
LABEL DIMENSIONS ARE NOMINAL - APPROXIMATELY 4” (102 MM) HIGH BY 6” (152 MM) WIDE
0
0
38 mm
(1.5 in)
96.5 mm
(3.8 in)
48 mm
1.89 in
102 mm
(4.02 in)
106 mm
(4.17 in)
24.4 mm
(1.0 in)
38.1 mm
(1.5 in)
50.8 mm
(2.0 in)
76.2 mm
(3.0 in)
*
A1
FROM
A2
TO
E1
2D
BAR CODE
D1
5J LICENSE PLATE
1D BAR CODE
D2
LOGISTICS
DATA
MIXED
LOAD
PAGE 24
AT 1724-C: LABEL
TEMPLATE FOR MIXED LOAD CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET WHEN MORE THAN ONE PART NUMBER IS CONTAINED BY THE MASTER CONTAINER OR PALLET.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
PART A
PART B
PART C
PART D
PART E
PART F
PART G
PART H
73.2 mm
1.5 IN
109.8 mm
4.5 IN
1724-C
15AUG2015
2015-08

## Slide 25
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
PHONE CONTACT #
MADE IN/ASSENBLED IN
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
LICENSE PLATE (5J):
UN 123456789 A2B4C6D8E
MIXED
LOAD
GROSS
WEIGHT:
9999
KG
DOCK 33
5
PART NUMBER
TOTAL QTY
12345678 1000
# PACKS
QTY PER # PACK
@
200
5
PART NUMBER
TOTAL QTY
00345678 100
# PACKS
QTY PER # PACK
@
20
5
PART NUMBER
TOTAL QTY
12245678 1000
# PACKS
QTY PER # PACK
@
200
10
PART NUMBER
TOTAL QTY
12045678 1000
# PACKS
QTY PER # PACK
@
100
5
PART NUMBER
TOTAL QTY
12005678 1000
# PACKS
QTY PER # PACK
@
200
6
PART NUMBER
TOTAL QTY
02345678 1200
# PACKS
QTY PER # PACK
@
200
5
PART NUMBER
TOTAL QTY
12345600 6000
# PACKS
QTY PER # PACK
@
1200
5
PART NUMBER
TOTAL QTY
10345678 750
# PACKS
QTY PER # PACK
@
150
FONTS SHALL BE UPPER CASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
EDI DATA SOURCES
ADDRESS INFORMATION
SUPPLIER GENERATED BASED ON CUSTOMER ORDER
DOCK CODE FROM
EDIFACT DELFOR LOC SEGMENT
DATA FROM SUPPLIER FILES
ATI PART NUMBER MUST MATCHGM ORDER
SUPPLIER DUNS ID COMBINED WITH SUPPLIER GENERATED SHIP PACK SERIAL NUMBER
DATA FROM SUPPLIER FILES
NOTE: SUPPLIER CONTACT (PHONE OR E-MAIL) IS AT THE SUPPLIER’S OPTION
LOGISTICS DATA
GROSS WEIGHT:
SUPPLIER GENERATED ROUND – NO DECIMAL
PAGE 25
AT 1724-C: LABEL
TEMPLATE FOR MIXED LOAD CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET WHEN MORE THAN ONE PART NUMBER IS CONTAINED BY THE MASTER CONTAINER OR PALLET.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-C
15AUG2015
2015-08
Notes: 3

## Slide 26
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
PHONE CONTACT #
MADE IN/ASSENBLED IN
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
LICENSE PLATE (5J):
UN 123456789 A2B4C6D8E
MIXED
LOAD
GROSS
WEIGHT:
9999
KG
DOCK 33
5
PART NUMBER
TOTAL QTY
12345678 1000
# PACKS
QTY PER # PACK
@
200
5
PART NUMBER
TOTAL QTY
00345678 100
# PACKS
QTY PER # PACK
@
20
5
PART NUMBER
TOTAL QTY
12245678 1000
# PACKS
QTY PER # PACK
@
200
10
PART NUMBER
TOTAL QTY
12045678 1000
# PACKS
QTY PER # PACK
@
100
5
PART NUMBER
TOTAL QTY
12005678 1000
# PACKS
QTY PER # PACK
@
200
6
PART NUMBER
TOTAL QTY
02345678 1200
# PACKS
QTY PER # PACK
@
200
5
PART NUMBER
TOTAL QTY
12345600 6000
# PACKS
QTY PER # PACK
@
1200
5
PART NUMBER
TOTAL QTY
10345678 750
# PACKS
QTY PER # PACK
@
150
FONTS SHALL BE UPPER CASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
NON-EDI DATA SOURCES
ADDRESS INFORMATION
SUPPLIER GENERATED BASED ON CUSTOMER ORDER
DATA FROM SUPPLIER FILES
ATI PART NUMBER MUST MATCHGM ORDER
SUPPLIER DUNS ID COMBINED WITH SUPPLIER GENERATED SHIP PACK SERIAL NUMBER
DATA FROM SUPPLIER FILES
NOTE: SUPPLIER CONTACT (PHONE OR E-MAIL) IS AT THE SUPPLIER’S OPTION
LOGISTICS DATA
GROSS WEIGHT:
SUPPLIER GENERATED ROUND – NO DECIMAL
PAGE 27
AT 1724-C: LABEL
TEMPLATE FOR MIXED LOAD CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET WHEN MORE THAN ONE PART NUMBER IS CONTAINED BY THE MASTER CONTAINER OR PALLET.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-C
15AUG2015
2015-08
Notes: 3

## Slide 27
FROM:
FROM ADDRESS LINE 1
FROM ADDRESS LINE 2
FROM ADDRESS LINE 3
FROM ADDRESS LINE 4
PHONE CONTACT #
MADE IN/ASSENBLED IN
TO:
TO ADDRESS LINE 1
TO ADDRESS LINE 2
TO ADDRESS LINE 3
TO ADDRESS LINE 4
DOCK:
LICENSE PLATE (5J):
UN 123456789 A2B4C6D8E
MIXED
LOAD
GROSS
WEIGHT:
9999
KG
DOCK 33
5
PART NUMBER
TOTAL QTY
12345678 1000
# PACKS
QTY PER # PACK
@
200
5
PART NUMBER
TOTAL QTY
00345678 100
# PACKS
QTY PER # PACK
@
20
5
PART NUMBER
TOTAL QTY
12245678 1000
# PACKS
QTY PER # PACK
@
200
10
PART NUMBER
TOTAL QTY
12045678 1000
# PACKS
QTY PER # PACK
@
100
5
PART NUMBER
TOTAL QTY
12005678 1000
# PACKS
QTY PER # PACK
@
200
6
PART NUMBER
TOTAL QTY
02345678 1200
# PACKS
QTY PER # PACK
@
200
5
PART NUMBER
TOTAL QTY
12345600 6000
# PACKS
QTY PER # PACK
@
1200
5
PART NUMBER
TOTAL QTY
10345678 750
# PACKS
QTY PER # PACK
@
150
FONTS SHALL BE UPPER CASE BOLD ARIAL NARROW, HELVETICA CONDENSED OR EQUIVALENT
Title: FROM:
6 Point, 1.5 mm, 0.06"
Address 4 lines max
10 point, 2.5 mm, 0.1"
Phone Number (Optional)
10 Point, 2.5 mm, 0.1"
MADE IN XXX or ASY IN XXX
10 Point, 2.5 mm, 0.1"
Title: None
PDF 417 2D Bar Code per AIAG B-16
Title: LICENSE PLATE (5J)
6 Point, 1.5 mm, 0.06"
Bar Code
Code 128
0.381 mm (15 mil) nominal
Height 13 mm (0.5 inch) min
Data Identifier: 5J
Assigning Authority: UN = D-U-N-S
9 digits D-U-N-S Number
9 characters container serial
number max
Human Readable Text
24 Point , 6.1 mm, 0.24”
Note-Spaces are optional in human readable text only. SPACES SHALL NOT BE INCLUDED IN BAR CODE DATA
Logistics Data:
Title: GROSS
WEIGHT
6 Point, 1.5 mm, 0.06”
Gross Weight Text
44 Point, 6.4 mm, 0..25”
Unit of Weight Text KG
44 Point, 6.4 mm, 0..25”
Title: TO:
6 Point, 1.5 mm, 0.06"
Address 4 lines max
12 Point, 4.3 mm, 0..17”
Title ; DOCK
6 Point, 1.5 mm, 0.06"
Dock Text
8 Character max
28 Point, 6.4 mm, 0..25"
1724-C FORMAT & FONT SPECS
Title: PART NUMBER
8 Point, 1.5 mm, 0.06"
Part Number Text
16 Point, 11.2 mm, 0.44”
Title: TOTAL QTY
8 Point, 1.5 mm, 0.06"
Total Qty Text
16 Point, 11.2 mm, 0.44”
Title: # PACKS
8 Point, 1.5 mm, 0.06“
# Packs Text
16 Point, 11.2 mm, 0.44”
Title: QTY PER PACK
8 Point, 1.5 mm, 0.06“
Qty Per Pack Text
16 Point, 11.2 mm, 0.44”
PAGE 27
AT 1724-C: LABEL
TEMPLATE FOR MIXED LOAD CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET WHEN MORE THAN ONE PART NUMBER IS CONTAINED BY THE MASTER CONTAINER OR PALLET.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
15AUG2015
2015-08
Notes: 4

## Slide 28
DATA IDENTIFIERS
DATA IDENTIFIERS (DIs) DEFINE THE NATURE OF THE DATA CONTAINED WITHIN THE LINEAR BAR CODE.
DIs ARE USED WITHIN THE 2D BAR CODE TO DEFINE THE NATURE OF THE DATA IN EACH FIELD.
THE TABLE BELOW REPRESENT TYPICAL DIs USED WITH ATI COMMON GLOBAL SHIPPING LABEL TEMPLATES.
ADDITIONAL DIs MAY BE USED AS BUSINESS PROCESSES REQUIRE AND SHALL CONFORM TO AIAG B10, B14, ANSI, AND ISO STANDARDS
PAGE 28
AT 1724-C: LABEL
TEMPLATE FOR MIXED LOAD CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET WHEN MORE THAN ONE PART NUMBER IS CONTAINED BY THE MASTER CONTAINER OR PALLET.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
1724-C
15AUG2015
2015-08
REQUIRED
OPTIONAL
OPTIONAL
OPTIONAL
REQUIRED
OPTIONAL
REQUIRED
REQUIRED
REQUIRED
WITHIN 2D BAR CODE
7Q10GT
USES ANSI X12 QUALIFILIER AS LAST TWO CHARACTERS TO DEFINE UNIT OF MEASURE
GT=GROSS KILOGRAMS
GROSS WEIGHT
7Q
BKLT3214
ATI SPECIFIED CONTAINER NUMBER OR IF NOT SPECIFIED USE SUPPLIER REFERENCE SUCH AS CARTON
CONTAINER TYPE
B
15KG1155
IF USED AS PART OF ATI BUSINESS PROCESS
KANBAN NUMBER
15K
KGM1234-00120
IF USED AS PART OF ATI BUSINESS PROCESS
PO NUMBER & PO LINE NUMBER
K
LC 15C
IDENTIFIES DELIVERY DOCK
DOCK CODE
21L
20LA6-987
DELIVERY LOCATION WITHIN PLANT
MATERIAL HANDLING CODE
20L
5JUN123456789A2B4C6D8E
HAS STRUCTURE (SEE PAGE 7 of 11)
LICENSE PLATE INDIVIDUAL CONTAINER OF LIKE PARTS
5J
Q160
TYPICALLY EXPRESSED IN PIECES
QUANTITY
Q
P12345678
TYPICALLY EIGHT (8) NUMERIC CHARACTERS
ATI PART NUMBER
P
EXAMPLE
COMMENT
DEFINITION
DATA IDENTIFIER
DI
2S
SHIPMENT ID (SID)/PICK-UP
SHEET NUMBER
CREATED BY SUPPLIER AND TRANSMITED IN
THE ASN
B03456789
OPTIONAL
Notes: 8

## Slide 29
PAGE 29
AT 1724-C: LABEL
TEMPLATE FOR MIXED LOAD CONTAINERS
LABEL PURPOSE/USE: TO BE USED ON A MASTER CONTAINER OR PALLET WHEN MORE THAN ONE PART NUMBER IS CONTAINED BY THE MASTER CONTAINER OR PALLET.
ATI WORLD-WIDE PURCHASING
ALL ATI FACILITIES (GLOBALLY)
AUTHORIZATION:
NOTE: ANY DIMENSIONS THAT ARE NOT OTHERWISE SPECIFIED ON THIS PAGE SHALL BE IN COMPLIANCE WITH AUTOMOTIVE INDUSTRY STANDARDS
CUSTOMER NAME:
SPECIFICATION ID NUMBER:
ISSUE DATE:
VERSION . RELEASE
Message Trailer EOT
Message Header [)>RS
M
E
S
S
A
G
E
E
N
V
E
L
O
P
E
5JUN123456789A2B4C6D8EGS7Q9999GTGS21LLC 15C
Format Header 06GS
Format Trailer RS
Format Header 06GS
Format Trailer RS
Format Header 06GS
Format Trailer RS
Format Header 06GS
Format Trailer RS
Format Header 06GS
Format Trailer RS
Format Header 06GS
Format Trailer RS
Format Header 06GS
Format Trailer RS
Format Header 06GS
Format Trailer RS
Format Header 06GS
Format Trailer RS
P12345678GS7Q1000PLGTGS7Q5PKGSQ200
P02345678GS7Q1200PLGTGS7Q6PKGSQ200
P12245678GS7Q1000PLGTGS7Q5PKGSQ200
P12045678GS7Q1000PLGTGS7Q10PKGSQ100
P10345678GS7Q750PLGTGS7Q5PKGSQ150
P12045600GS7Q6000PLGTGS7Q5PKGSQ1200
P00345678GS7Q100PLGTGS7Q5PKGSQ20
P12005678GS7Q1000PLGTGS7Q5PKGSQ200
[)>RS06GS5JUN123456789A2B4C6D8EGS7Q9999GTGS
21LLC 15CRS06GSP12345678GS7Q1000PLGTGS7Q5PKGS
Q200RS06GSP02345678GS7Q1200PLGTGS7Q6PKGSQ200RS
06GSP12245678GS7Q1000PLGTGS7Q5PKGSQ200RS06GS
P12045678GS7Q1000PLGTGS7Q10PKGSQ100RS06GSP10345678GS
7Q750PLGTGS7Q5PKGSQ150RS 06GSP12045600GS7Q6000PLGTGS
7Q5PKGSQ1200RS06GSP00345678GS7Q100PLGTGS7Q5PKGSQ20RS
06GSP12005678GS7Q1000PLGTGS7Q5PKGSQ200RSEOT
RS
2D BAR CODE
DATA STRUCTURE
1724-C
15AUG2015
2015-08